## Slide 1
EDR100
Electrical Drivelines 1
HT2023
Danyang Cui
Lecture 5

## Slide 2: Course outline
Course intro, tools, getting started with simulations
Vehicle behaviors and simulation tricks, drive cycles
Simulation of Electric Machine with MotorCAD data
Simulation of Power Electronics and Battery
Full vehicle behavior, final assignment

## Slide 3: Lecture 5 outline
Scaling of components
  PEC
  EM
  Battery
New/different vehicles
New/different drive cycles
Assignment 5

## Slide 4: Electrical Drive Systems
RESS
(Battery)
PEC
(Power Electric Converter)
EM
(Electric machine)
GB + DIFF
(Gearbox & differential)
Image courtesy: BorgWarner
Image source: EV Tech Explained
Image courtesy: BorgWarner
Image courtesy: Siemens
Tire(s)
Image courtesy: Volvo Cars

## Slide 5: System overview
(max performance limits)
Inverter
Battery
system
Gearbox
Differential
Wheel
Wheel
Electric
Machine
Real Power Voltage Current
Complex Power
3xVoltage 3xCurrent
Frequency Amplitude Phase delay
Mechanical
Power, Speed, Torque, Force
𝑉𝐷𝐶 (V)
𝐼𝐷𝐶 (A)
𝑃𝐷𝐶 (W)
𝑉𝐴𝐶 (V)
𝐼𝐴𝐶 (A)
𝑆𝐴𝐶 (VA)
3x
3x
Ω𝐸𝑀 (rad/s)
τ𝐸𝑀 (Nm)
𝑃𝐸𝑀 (W)
3x
Ω𝐺𝐵 (rad/s)
τ𝐺𝐵 (Nm)
𝑃𝐺𝐵 (W)
𝐹𝐿 (N)
𝑣𝐿 (m/s)
𝐹𝑅 (N)
𝑣𝑅 (m/s)
Ω (rad/s)
𝐿
𝜏𝐿 (Nm)
𝑃𝐿 (W)
Ω𝑅 (rad/s)
𝜏𝑅 (Nm)
𝑃𝑅 (W)
Road
Road
Electrical
Electric drive: DC in, torque out

## Slide 6: Scaling of PEC
Image courtesy: BorgWarner

## Slide 7: Scaling of PEC in Simulink
Scaling of PEC in Simulink model
Parameter “PEC_scaling” in init-file
  Scales the internal resistance of the IGBT transistors and diodes  Lower conduction losses
  Scales the maximum current
PEC_scaling = 2 means:
  Twice the size of transistors working in parallel
  “Two inverters in parallel”, effectively sharing the
EM current equally and reducing the losses
Image courtesy: BorgWarner
Image courtesy: Infineon
Image courtesy: Infineon

## Slide 8: Scaling of PEC
What happens if only the PEC is scaled, with total losses?
What determines the minimum PEC scaling to be used?
  Maximum current
What determines the maximum PEC scaling to be used?
  Secondary effects not presented in Simulink model, e.g. cost, size, weight

## Slide 9: Scaling of EM
Image courtesy: Siemens

## Slide 10: Scaling of EM
EM_scaling will scale the
EM’s torque capability, but leave the speed characteristics and max power unchanged
This corresponds to changing the length of the EM
Scaling the EM will make the same output power (but different torque and speed) have a different efficiency
EM_scaling
Scaling = 0.5

## Slide 11: Scaling of Battery System

## Slide 12: Battery system scaling
Feel free to experiment with:
Cell charge capacity (ESS_cell_Qmax)
  To scale charge- and energy capacity of individual cells
  Secondary effect: Larger capacity in cells means more mass, see ESS_cell_mass
Parallel connection of cells (ESS_cells_parallel)
  To scale charge- and energy capacity of system
Cell internal resistance scaling (ESS_cell_R_scaling)
  To scale battery losses, and indirectly; current limits
  Secondary effects (not in Simulink model): Lower resistance will need bigger, heavier and more expensive cells
Cell max/min current limits (ESS_cell_Cvalue)
  To scale maximum power capacity
  Secondary effects (not in Simulink model): Higher C-value will need bigger, heavier and more expensive cells
What NOT to change (not the scope of this course)
System voltage (stay with 400 V max)
Cell OCV curve

## Slide 13: Gearbox scaling
Image courtesy: GKN
Image courtesy: GKN

## Slide 14: Gearbox scaling
Feel free to experiment with:
Gear ratio (gear_ratio)
Gearbox efficiency (eta_gear)
  To add or decrease gearbox losses
Remember to check for boundary conditions, e.g:
What is the maximum speed the vehicle can drive with the EM limits?
Can the EM deliver the maximum torque needed?

## Slide 15: Vehicle parameters

## Slide 16: Vehicle parameters
Feel free to experiment with:
Vehicle mass (m_v)
Wheel effective diameter (d_wheel)
Wheel rolling resistance (c_r)
Aerodynamic frontal area (A_f)
Aerodynamic drag coefficient (c_d)
Parameter | Reference car | Medium Truck
m_v (kg) | 1 700 | 6 000
d_wheel (m) | 2.101/pi*0.97 | 2.101/pi*0.97
c_r (-) | 9.0*10-3 | 9.0*10-3
A_f (m^2) | 2.3 | 5.0
c_d (-) | 0.28 | 0.6
Reference parameters from Lecture 1 and Assignment 4

## Slide 17: Drive cycles
So far, we have used WLTC for simulation. What if we use another drive cycle?
How will it affect energy consumption?
How will it affect component efficiency?
Think about making your own drive cycle or “mission profile”, e.g:
0-100 km/h acceleration
Decide what 0-100 km/h time to achieve (dt)
Calculate average acceleration a = dv/dt
Make your own speed profile with a ramp from 0-100 km/h
Examples of acceleration times for production cars
(https://www.engineeringtoolbox.com/car-acceleration-d_1309.html)

## Slide 18: Assignment 5
Parameter analysis using Simulink Model 4
See Word-template in Canvas.