## Slide 1: EDR100 Electrical Drivelines 1
HT2023
Danyang Cui
Lecture 4

## Slide 2: Course outline
Course intro, tools, getting started with simulations
Vehicle behaviors and simulation tricks, drive cycles
Simulation of Electric Machine with MotorCAD data
Simulation of Power Electronics and Battery
Full vehicle behavior, assignments & groups

## Slide 3: Lecture 4 outline
Power Electronic Converter (PEC)
Battery / Energy Storage Systems (ESS)
Assignment 4

## Slide 4: Electrical Drive Systems
RESS
(Battery)
PEC
(Power Electric Converter)
EM
(Electric machine)
GB + DIFF
(Gearbox & differential)
Image courtesy: BorgWarner
Image source: EV Tech Explained
Image courtesy: BorgWarner
Image courtesy: Siemens
Tire(s)
Image courtesy: Volvo Cars

## Slide 5: System overview
Inverter
Battery
system
Gearbox
Differential
Wheel
Wheel
Electric
Machine
Real Power Voltage Current
Complex Power
3xVoltage 3xCurrent
Frequency Amplitude Phase delay
Mechanical
Power, Speed, Torque, Force
𝑉𝐷𝐶 (V)
𝐼𝐷𝐶 (A)
𝑃𝐷𝐶 (W)
𝑉𝐴𝐶 (V)
𝐼𝐴𝐶 (A)
𝑆𝐴𝐶 (VA)
3x
3x
Ω𝐸𝑀 (rad/s)
τ𝐸𝑀 (Nm)
𝑃𝐸𝑀 (W)
3x
Ω𝐺𝐵 (rad/s)
τ𝐺𝐵 (Nm)
𝑃𝐺𝐵 (W)
𝐹𝐿 (N)
𝑣𝐿 (m/s)
𝐹𝑅 (N)
𝑣𝑅 (m/s)
Ω (rad/s)
𝐿
𝜏𝐿 (Nm)
𝑃𝐿 (W)
Ω𝑅 (rad/s)
𝜏𝑅 (Nm)
𝑃𝑅 (W)
Road
Road
Electrical
Electric drive: DC in, torque out

## Slide 6: Power Electronics
For Electric Vehicles

## Slide 7: Naming convention
In my slides: “Traction Inverter”
“Inverter” (DC-->AC)
“Motor Controller”
PEC = Power Electronic Converter
PEM = Power Electronic Module
VSC = Voltage Source Controller
All names refer to the same component!
Image source: Koenigsegg Motor Controller called “David”, 2022
Interesting tips:
DC -> AC: Inverter
DC -> DC: Converter
AC -> AC: Converter
AC -> DC: Rectifier
“Converter” applies to all.

## Slide 8: Purpose of power electronics
Convert direct voltage to alternating voltage
  Battery – to – Three-phase EM
  Efficiency and reliability very important
Control torque and speed of EM
  Use of high-precision, high-speed feedback control
  Torque (current) closed-loop control usually utilized
Safety
Never unintentionally panic brake
Never unintentionally accelerate
EM = Electric Machine
REESS |  | PEC |  | EM
Direct Voltage
3-phase voltage
Torque &
speed
REESS = Rechargeable Electrical Energy Storage System (Traction Battery)

## Slide 9: Schematic overview of PEC
Electrical topology:
Two-level, three phase inverter
Use six individually controlled power semiconductor switching units
(e.g. IGBTs or MOSFETs)
One phase leg (two switches) can generate a phase voltage of:
• +Udc/2
-Udc /2
(and nothing else)
Each pair of phase legs can generate only a line-to-line voltage of:
-Udc
0
• +Udc
(and nothing else)
Traction Battery
T1
T2
T4
T6
D1 T3
D3 T5
D5
D2
D4
D6
A
B
C
Electric
machine
Udc
+
2
-
Udc
2
0
Traction Inverter
(line voltage)
- +
UA
(phase voltage)
-
+
UB−𝐶

## Slide 10: Pseudo-sinusoidal voltage with PWM
PWM (Pulse Width Modulation) can be created by comparing a triangular carrier wave and a reference sinusoidal wave.
u
+½Udc
0
1,0
0,7
-½Udc
p
Reference wave
Carrier wave
Rotor angle
PWM voltage to one EM phase
v
Logic rule:
If reference wave > carrier wave:
Enable high transistor
Switch period
Commonly
0.1 ms = 10 kHz
p
2p
2p

## Slide 11: Traction Inverter video
“A Look Inside The Tesla Model 3, Chevy Bolt, and BMW i3”
(11:37-14:20)
https://youtu.be/pgu6mkKZwNg?t=697

## Slide 12: Traction Inverter overview
Source: “A scalable life cycle inventory of an automotive power electronic inverter unit—part I: design and composition”, Anders Nordelöf et. al. 2018

## Slide 13: Traction Inverter example: BMW i3
Source: “Oak Ridge National Laboratory Annual Progress Report for the Electric Drive Technologies Program”, Oak Ridge National Laboratory, October 2016
13 (34)

## Slide 14: Simulating IGBT inverters
IGBTs display these losses:
  Forward channel
voltage drop
  Forward resistive voltage drop
  Reverse diode conduction
  Diode reverse recovery
Which means IGBTs behave like two different diodes for each direction of conduction.
Image source: “Applying IGBTs“ ABB Application Note 5SYA 2053-04
D2
T1
D2
T1

## Slide 15: Assumptions in Simulink PEC Model
PEC operates “quasi static” = Individual PWM steps are not
modeled in time. Instead, replaced by general loss formulas
Losses based on operating point of EM:
  Phase voltage
  Phase current
  Power factor
  Feed voltage (constant)
IGBT (Insulated Gate Bipolar Transistor) parameters implemented from datasheet of high-performance automotive module found in several popular EVs currently on the market

## Slide 16: Example power module used in Simulink block
Infineon is one of the market-leading automotive power electronic parts suppliers
  Their current automotive offer can be found here: https://www.infineon.com/cms/en/product/power/igbt/ automotive-qualified-igbts/automotive-igbt-modules/
IGBT “Six-pack”

## Slide 17
IGBT model
One of the most powerful 6-pack is FS820, with direct water-cooling fins. All loss parameters are extracted from the product data sheet.

## Slide 18: Battery Systems
“Traction Battery”, “REESS”, “ESS”

## Slide 19: EV battery system examples
Chevrolet Bolt
Nissan Leaf
Volkswagen Golf GTE
BMW i3

## Slide 20: Battery system overview
Pack
Module
BMS
Cells
Cooling
Frames
End cover
Pictures from Volvo Cars R&D project “BatMan” – Public final report

## Slide 21: Cell formats
Prismatic
Hard shell (plastic/metal) Super-high charge capacity High energy density
Pouch
Soft shell (plastic/Alu-foil) High charge capacity
Very high energy density
Cylindrical
Semi-hard shell (Alu/steel) Low charge capacity
Very high energy density

## Slide 22: Some battery pack numerical
Cells will need to be connected in series and parallel to form an EV pack
Parallel connection will increase charge capacity (Ah)
Series connection will increase voltage (V)
  Pack maximum voltage: Cell maximum voltage * number of cells in series
Cells will form about 66% of the mass of the entire pack, the rest is enclosure, protection, electronics, fuses, connectors, etc.
Assadian, Francis & Mallon, Kevin & Walker, Brian. (2019). New Energy Management Concepts for Hybrid and Electric Powertrains: Considering the Impact of Lithium Battery and Ultracapacitor Aging. 10.5772/intechopen.83770.
Each cell holds the maximum energy:
  Max charge capacity (Ah) * Nominal voltage (V) = Max Energy (Wh)

## Slide 23: Electrical modeling basics
Thevenin equivalent = Ideal voltage source + internal resistance
Results:
Discharge current  Internal voltage drop  Heat (i2*R0)
Stop drawing current 
Voltage jumps back to Open Circuit Voltage
Open circuit
voltage

## Slide 24: Electrical modeling basics
Never measure cell, module or pack resistance directly!
A starter battery (12V) may be discharged at 50A for a second or longer.
A traction battery pack (400-800V) may be discharged at an extremely high current.
Special measuring instruments must be used.
Ω

## Slide 25: Open Circuit Voltage
Features of simple model:
OCV vs SOC + chemistry
R vs temperature
0
R0 sometimes also called Rint
LTO
LTO
Ref: Cell measurements from Chalmers’ lab by Stefan Skoog.
NMC
LCO
NMC

## Slide 26: R0 depends on cell type
Even when adjusting for size and capacity, R0 has a large spread
NMC
LTO
LTO
LCO
NMC
Ref: Cell measurements from Chalmers’ lab by Stefan Skoog.

## Slide 27: R0 typical behavior
Internal resistance increases with lower temperature
  Slower chemical
reactions
Arrhenius behavior
How steep depends on cell design, chemistry, materials
-20 -10 0
Ref: Cell measurements from Chalmers’ lab by Stefan Skoog
20
40
°C
R
0
(P.U.)
1
3
12
25
10

## Slide 28: Aging parameter
Internal resistance increases with age
  Except at the very beginning of life
“Age” = k0*Calendar time + k1*Number of cycles
A “cycle” is all energy in a complete charge + discharge procedure
 Amount of charge or energy turnaround

## Slide 29: Installed vs available capacity
The full datasheet value is almost never used!
Lifetime of battery cells is more important than the best charge cycle
100%
85%
60%
Installed ”datasheet” capacity
High-energy application (EV or PHEV)
High-power application (HEV or mHEV)

## Slide 30: Parameter extraction
…and more advanced models, for reference.

## Slide 31: R0 test methods Pulse testing
EIS
Equivalent electrical model
Battery cell
EIS = Electrochemical Impedance Spectroscopy

## Slide 32: Battery models
Simple model: Internal Voltage and R
  Enough accuracy for this course
  Fairly easy to get data from battery suppliers
More advanced model: Internal Voltage & R & 2RC
  Captures most battery time dynamics in drive cycles
  Should be used for high accuracy simulations
  Hard to get data: Must measure yourself, using pulse testing or EIS

## Slide 33: Example cell for Simulink model
US EV-only brand
Cylindrical cells, size 2170
Can be parallel connected and series
connected to form any EV battery size
A typical entry-level EV contain 2976 pcs of these cells
0.070 kg each
Ca 5.0 Ah each
3.65 V nominal (50 % SOC)
4.15 V maximum (100 % SOC)
2.80 V minimum (0 % SOC)
Measurement data from Chalmers’ lab, Torbjörn
Thiringer’s research team. With permission.
Electrochemical Impedance Spectroscopy measurement
At room temperature, 50 % SoC, new cell.
Mass-produced cell by well-known
Impedance at
0.1 Hz = 10 s long pulse
R0 = 22 mOhm

## Slide 34: Assignment 4
PEC, ESS and Simulink Model4