## Slide 1: EDR100 Electrical Drivelines 1
HT2023
Danyang Cui
Lecture 1

## Slide 2: General course info (1/2)
Language
English (written and spoken)
Teachers
Danyang Cui, danyang.cui@hv.se
Examiner
Boel Ekergård, boel.ekergard@hv.se
Questions/consultations
Use Canvas messages or emails for private questions.
Credits
5.0 ECTS
Contents
5 lectures
5 exercise/support sessions with teacher
1 group project with 2 people in a group
Calendar
Kronox / Canvas
Literature & study material
Slides from lectures.
Available in Canvas after each lecture.

## Slide 3: General course info (2/2)
Examination
Course grades: U/3/4/5
1 individual hand-in calculation assignment per lecture, totally 5
1 group project with written report and oral presentation including individual opposition
Other
This course is very related to a course held VT2022 at HV: EDS600 - Electrical Drive Systems
VT2022 at HV: EKE600 - Electric Vehicles,
Power electronics and electrical motors
Typical lecture layout
45 min slides + theory (15 min break)
45 min examples and demo
Question sessions can be used to ask questions
from current or previous course module!

## Slide 4: Course outline
Course intro, tools, getting started with simulations
Vehicle behaviors and simulation tricks, drive cycles
Simulation of Electric Machine with MotorCAD data
Simulation of Power Electronics and Battery
Full vehicle behavior, assignments Q&A
Results, presentations, summary, conclusions

## Slide 5: Teacher intro
Main teacher
Danyang Cui
PhD student E.E. at Uppsala Univ.
Topic: Non-rare earth traction motor design for EV
M.Sc. E.E. 2017, University of Tokyo
Research field: Wireless Power Transfer for EV
2017-2021: Volvo Trucks Japan
Examiner
Boel Ekergård
HV Profile Associate Professor
Division of Industrial Engineering and Management,
Electrical- and Mechanical Engineering

## Slide 6: Course motivation
Background
Plug-in EVs offer the biggest potential of offering the lowest carbon footprint of any personal transport means
Plug-in electric vehicles are increasing drastically in popularity
Outlook
Several automakers are limiting or shutting down the development of internal combustion engines
The vast majority of car brands now offer at least one EV model
Emission-free zones are, or will be, implemented in densely populated areas in the world
The western world is moving rapidly towards electricity production through low-carbon solutions

## Slide 7: Typical problem to solve in this course
How much power, torque, force is required to propel a typical vehicle?
What components, parameters, models are important?
How much power, energy is needed in a drive cycle?
How does drive cycles affect powertrain dimensioning?
What is a typical energy efficiency for an electric vehicle?

## Slide 8: Scope of course (1/2)
Electrification is relevant to all vehicle types.
This course will focus on light passenger vehicles, a.k.a. cars.

## Slide 9: Scope of course (2/2)
Internal combustion engines (ICE) are becoming less relevant (for most cars)
Hybrid cars are very complicated to model, especially the control part!
Electric powertrains are much easier to model than ICE systems
  No gearbox!
ICE
7-step
GB
DIFF
ESS
EM
PEC
C1
C2
C = Controlled clutch
DIFF = Differential
EM = Electric Machine
ESS = Energy Storage System GB = GearBox (transmission)
ICE = Internal Combustion Engine
PEC = Power Electric Converter (motor controller)
GB
PEC
EM
ESS
DIFF
VW Passat GTE Plug-in hybrid
Tesla Model 3 SR+ Plug-in electric

## Slide 10: Terms and abbreviations
Term | Explanation
Propulsion system | All components working together to propel the vehicle. E.g. ICE, gearbox, differential, energy/fuel storage, electric machine.
Traction system | See Propulsion system
EM | Electric Machine (motor + generator)
GB | GearBox
PEC | Power Electronic Converter, Inverter, Motor Controller
ESS | Energy Storage System, e.g. battery pack
ICE | Internal Combustion Engine
xEV | Any electrified vehicle: HEV, PHEV, FCEV, mHEV
HEV | Hybrid Electric Vehicle (not plug-in charging capable)
mHEV | Mild Hybrid Electric Vehicle
PHEV | Plug-in Hybrid Electric Vehicle
FCEV | Fuel-Cell Electric Vehicle
EDU | Electric Drive Unit – System of Electric Machine, Power Electronics, Control and Gearbox

## Slide 11: Electrical Drive Systems
ESS
(Battery)
PEC
(Power Electric Converter)
EM
(Electric machine)
GB + DIFF
(Gearbox & differential)
Image courtesy: BorgWarner
Image source: EV Tech Explained
Image courtesy: BorgWarner
Image courtesy: Siemens

## Slide 12: System Simulation tools
How can we set up and calculate energy flow accurately in multi- component systems?
1. Hand calculations
Very explicit, free cost
Very slow to execute, prone to mistakes
2. Programming
(e.g. C++,C#, Java, Python, Matlab)
Explicit, free cost, very fast to execute
Requires experience to avoid mistakes
3. Graphical Programming
(e.g. Simulink, SimScape, OpenModelica, SciLAB, Xcos)
Very fast to execute, easy to overview, modular
Less explicit, lots of software to install, licenses

## Slide 13: Model-based approach
Backwards-simulation
“We know the answer, let’s figure out what the best operating point was”
Forward-simulation
“We know where we want to go, let’s figure out all the details in all the components to get roughly there”
Very fast, simple model
Does not take time dynamics into account Ignores component limitations
Represents dynamics and limitations in sub- systems and internal components
Quite complicated to build model
Model solver often fails to converge Target speed will never exactly be reached

## Slide 14: Model Based Toolkits
This has been done before in…
Many 100s of PhD Theses…
Thousands of Master Theses…
(Tens of?) Thousands of research papers…
This course is highly inspired by “QSS-Toolbox”, made openly available by ETH Zürich, Institute for Dynamic Systems and Control:
https://idsc.ethz.ch/research-guzzella-
onder/downloads.html
Optional course literature.
Available to download through HV Library / Springer: https://discover.hv.se/iii/encore
/record/C Rb1260368

## Slide 15: Matlab
The main tools used in this course in lectures and assignments are:
Mathworks Matlab and Simulink version R2021a
You can access this tool in three ways as a University West student:
Install Matlab & Simulink on your own computer.
  See full guide: https://www.hv.se/en/student/it-services-and-support/available-software/matlab/
Use any computer to access an HV virtual computer room
  See full guide: https://www.hv.se/en/student/it-services-and-support/virtual-computer-rooms/
  All softwares are pre-installed
Go to a computer room and log in with your HV account
  All softwares are pre-installed

## Slide 16: Matlab version
The course contents are designed in R2021a.
If you have a newer or older version, there might be minor errors or minor functional differences in the files I will be distributing.
If you deviate from R2021a, any issues will be on your responsibility.
If you choose to install Matlab Simulink on your own computer(s), it should be enough to choose these toolboxes:
The basic installation requires about 9 GB of storage space.

## Slide 17: Basic vehicle dynamics theory
Longitudinal vehicle dynamics and bicycle models.

## Slide 18: What kinematic model to select?
Image courtesy: Stochastic Source Seeking by Mobile Robots, Shun-ichi Azuma et.al.
Car Bicycle
Image courtesy: The kinematic bicycle model: A consistent model for planning feasible trajectories for autonomous vehicles? - Polack et.al..
Image courtesy: Unicycle Kinematic Model - Mathworks.
Monocycle

## Slide 19: Monocycle model
Pros
Very simple equations
No non-linear dynamics
Only a small set of vehicle parameters needed
Limitations
Cannot be represented:
  Lateral motion
  Load shift front/rear
  Tire slip or skid
Not apt for racing situations
Note!
Only longitudinal forces represented!

## Slide 20: Forces on a car (bi-/monocycle model)
𝐹𝑡 = Traction force from motor(s) through wheels
𝐹𝑔 = Gravitational pull (e.g. uphill driving)
𝐹𝑟 = Rolling friction (from tires)
𝐹𝑎 = Aerodynamic drag
𝐹𝑑 = Other forces
𝑣 = Vehicle velocity over ground (m/s)
𝑚𝑣 = Total vehicle mass (kg)
𝑔 = Gravity of Earth (m/s²)
α = Slope angle (rad)
Image source: Vehicle Propulsion Systems, Guzzella, Sciarretta, 2007

## Slide 21: Forces and power balance equations (1/5)
Note:
𝑑
𝑣 𝑡+1 −𝑣(𝑡)
𝑑𝑡 𝑡+1 −𝑡
𝑣 (m/s) = = 𝑎 = acceleration (m/s²)
In plain text:
(1) The sum of all longitudinal forces acting on the car decides the rate of change in speed (i.e. acceleration) together with the total mass.
(1)
𝑑𝑣
𝐹𝑎𝑐𝑐 = 𝑚 ∙ 𝑎 = 𝑚 𝑑𝑡
𝑁 = 𝑘𝑔 ∙ 𝑚/𝑠2

## Slide 22: Forces and power balance equations (2/5)
In plain text:
(2) The total vehicle force is the Traction force created by the motor(s) subtracted by all the friction forces.
(2)
𝐹𝑡 = Traction force from motor(s) through wheels
𝐹𝑔 = Gravitational pull (e.g. uphill driving)
𝐹𝑟 = Rolling friction (from tires)
𝐹𝑎 = Aerodynamic drag
𝐹𝑎𝑐𝑐 = 𝐹𝑡 − 𝐹𝑎 + 𝐹𝑟 + 𝐹𝑔
𝑁 = 𝑁

## Slide 23: Forces and power balance equations (3/5)
In plain text:
(3) The required traction power is the product of the total vehicle force and vehicle speed.
(3)
𝑃𝑡 = 𝐹𝑡 ∙ 𝑣
𝑊 = 𝑁 ∙ (m/s)

## Slide 24: Forces and power balance equations (4/5)
In plain text:
(4) The total wheel torque is the Traction force multiplied with the effective wheel radius.
(4)
𝜏𝑤 = 𝐹𝑡 ∙ 𝑤𝑟
𝑁𝑚 = 𝑁 ∙ (m)

## Slide 25: Forces and power balance equations (5/5)
In plain text:
(5) The wheel rotational speed equals the vehicle ground speed divided by the effective wheel radius.
𝑤
(5) 𝜔
=
𝑣
𝑤
𝑟
𝑟𝑎𝑑/𝑠 = 𝑚/𝑠 / (m)

## Slide 26
Rolling Radius
𝜏𝑤 = 𝐹𝑡 ∙ 𝑤𝑟

## Slide 27: Tire parameters
Tire (or tyre, as the Brits prefer it) data, as simple as possible
Tires are the prime contact between powertrain and ground
  Represented by two parameters:
  Effective rolling radius
  Rolling friction
An ideal wheel is perfectly round and has no friction
  This approximation is good enough for railway applications (steel-to-steel)
  Rubber dressed wheels in cars deform under vertical load and wheel torque
  Parameters depend on speed (centrifugal forces), temperature, age (wear)

## Slide 28: Tire parameters
Standard car tire sizes are specified with a minimum of three numbers: Nominal section width, aspect ratio, wheel dimeter
Example: New Volvo V60
  235/45R18
  This is a very normal mid-size premium car tire size
  Calculate tire size with e.g.
https://tiresize.com/calculator/
 Tire circumference: 2101 mm unloaded
 What’s the effective wheel radius?
Picture source: https://www.calculator.net/

## Slide 29: Loaded tire
Remember, we still assume low loads and no aggressive driving
  Model does not apply for race driving
The most important parameter to respect is tire deformation due to load, even during fairly normal loads.
Picture source: Vehicle Dynamics Compendium 2017, Bengt Jacobson et al, Chalmers University
This leads to:
  Calculated circumference is larger than effective circumference
  𝑅𝑙2 < 𝑅0in scenario c)
  How much less?
    Ca 2-4% lower

## Slide 30: Tires, summary
Effective wheel radius 𝑟𝑤 is ca 97% of unloaded wheel radius
Unloaded wheel radius can be calculated from wheel dimensions,
e.g. 235/45R18. Use calculator to extract rolling circumference
Tires impose a rolling friction due to rubber deformation
  Friction will be assumed to be a function of only mass in our scope
Tires will change effective wheel radius with temperature, speed, vertical load, dynamic loads (load shifts)
  Those effects are negligible for the purpose of the scope of this course
Tires have transient behavior that will not be modeled in the scope of our course
  E.g. turning (lateral-to-longitudinal force interactions)
Tire slip will induce non-linearities and large losses in the tires
  Normal driving (drive cycles) means that slip can be ignored

## Slide 31: Rolling Friction 𝐹𝑡𝑜𝑡 = 𝐹𝑡 − 𝐹𝑎 + 𝐹𝑟 + 𝐹𝑔

## Slide 32: Rolling Friction
𝑐𝑟= Tire friction constant.
𝑔 = Gravity of Earth (m/s²)
α = Slope angle (rad)
E.g. 9.0 kg/ton = 0.009 (-)
E.g. 9.81 m/s²

## Slide 33: Rolling resistance numbers
Wikipedia:
  https://en.wikipedia.org/wiki/Rolling_resistance
  https://en.wikipedia.org/wiki/Low_rolling_resistance_tire

## Slide 34: Aerodynamics 𝐹𝑡𝑜𝑡 = 𝐹𝑡 − 𝐹𝑎 + 𝐹𝑟 + 𝐹𝑔
Image source: Automotive Aerodynamics - Joseph Katz - ISBN: 978-1-119-18572-7

## Slide 35: Aerodynamics
ρ𝑎= density of the ambient air
𝐴𝑓 = Vehicle equivalent frontal area (m²)
𝑐𝑑 = aerodynamic drag coefficient (-)
𝑣 = vehicle speed (m/s)
E.g. 1.225 kg/m3
E.g. 2.3 m²
E.g. 0.28
𝑘𝑚
90
E.g. 90 km/h = ℎ
3600 𝑠/ℎ
1000 𝑚/𝑘𝑚
= 25 𝑚/𝑠

## Slide 36: Aerodynamic drag 1/2
Sources for further reading
Automotive Aerodynamics Joseph Katz
ISBN: 978-1-119-18572-7
https://www.wiley.com/en- us/Automotive+Aerodynamics-p- 9781119185727
  Cd values example chapter: https://mechanixillustrated.technicacuriosa.com
/2017/03/04/an-introduction-to-automobile- aerodynamics/

## Slide 37: Aerodynamic drag 2/2
Wikipedia:
  https://en.wikipedia.org/wiki/Automotive_aerodynamics
  https://en.wikipedia.org/wiki/Automobile_drag_coefficient

## Slide 38: Hill driving and slopes 𝐹𝑡𝑜𝑡 = 𝐹𝑡 − 𝐹𝑎 + 𝐹𝑟 + 𝐹𝑔

## Slide 39: Hill driving / slopes
𝑚𝑣 = Total vehicle mass (kg)
𝑔 = Gravity of Earth(m/s²)
α = Slope angle (rad)
E.g. 1 700 kg
E.g. 9.81 m/s²
E.g. 0.07 rad (Hallandsåsen)
E.g. 0.31 rad (Highest slope in L.A, USA)

## Slide 40: Acceleration 𝐹𝑎𝑐𝑐 = 𝑚 ∙ 𝑎

## Slide 41: Acceleration
𝑚𝑣 = Total vehicle mass (kg)
𝑣 = Vehicle velocity (m/s)
𝑎 = Vehicle acceleration (m/s²)
E.g. 1 700 kg
E.g. 0..130 km/h = 0…36 m/s
E.g. ±2.5 m/s² for comfortable driving
𝑑
𝐹𝑎𝑐𝑐 = 𝑚𝑣 𝑑𝑡 𝑣 = 𝑚𝑣𝑎

## Slide 42: Vehicle mass
The model represent the vehicle as a point mass
For all road vehicles (cars, buses, trucks) a set of weights are defined:
  Dry weight (vehicle without fuels, oils or any payload)
  Curb weight (vehicle with fuel and a driver)
  Gross weight / GVM / GVWR (fully loaded / max weight)

## Slide 43: Vehicle mass
In our model, we use the service mass, i.e. curb weight
  Vehicle ready to go (fully charged/fueled, one driver, all basic equipment on vehicle), according to European Directive 95/48/EC.
ICCT – EU Vehicle Market Statistics
  https://theicct.org/publication/european-vehicle-market-statistics- 2021-2022/

## Slide 44: Assignment 1 Deadline: 1 week later

## Slide 45: Car definition for assignment 1
Constants
ρ𝑎 = 1.225 kg/m3
𝑔 = 9.81 m/s²
𝑐𝑟
𝑤𝑟
𝐴𝑓
𝑐𝑑
= 0.009
= 0.668/2 * 0.97 = 0.324 m
= 2.3 m²
= 0.28
𝑚𝑣 = 1 700 kg
This represents an average saloon car

## Slide 46: Assignment 1
Set up the formulas for all relevant forces in Matlab using M-files. Double check your calculation by hand calculations and/or spreadsheets. (𝐹𝑎𝑐𝑐, 𝐹𝑡, 𝐹𝑎, 𝐹𝑟, 𝐹𝑔)
With the car definition, calculate the outputs (𝐹𝑡, 𝜏𝑤, 𝑃𝑡) for all scenarios in this table:
Scenario |  | 𝒗 | 𝒂 | 𝜶 | 𝐹𝑡 | 𝜏𝑤 | 𝑃𝑡
1 | Slow speed driving | 10 km/h | 0 m/s² | 0 rad |  |  | 
2 | Medium speed driving | 50 km/h | 0 m/s² | 0 rad |  |  | 
3 | Freeway driving | 90 km/h | 0 m/s² | 0 rad |  |  | 
4 | Highway driving | 130 km/h | 0 m/s² | 0 rad |  |  | 
5 | Medium speed overtaking | 50 km/h | 2.5 m/s² | 0 rad |  |  | 
6 | High speed overtaking | 130 km/h | 1.0 m/s² | 0 rad |  |  | 
7 | Slow speed very high slope | 50 km/h | 0 m/s² | 0.31 rad |  |  | 
8 | High speed, high slope (“Hallandsåsen”) | 130 km/h | 0 m/s² | 0.07 rad |  |  |