## Slide 1
EDR100
Electrical Drive Systems
HT2023
Danyang Cui
Lecture 3

## Slide 2: Course outline
Course intro, tools, getting started with simulations
Vehicle behaviors and simulation tricks, drive cycles
Simulation of Electric Machine with MotorCAD data
Simulation of Power Electronics and Battery
Full vehicle behavior

## Slide 3: Lecture 3 outline
Electric Machines (EMs)
System overview
Type, parts, names
Electric properties, electric model
Typical performance of EMs
Performance examples
Design and modeling of EMs
Assignment 3

## Slide 4: Electrical Drive Systems
RESS
(Battery)
PEC
(Power Electric Converter)
EM
(Electric machine)
GB + DIFF
(Gearbox & differential)
Image courtesy: BorgWarner
Image source: EV Tech Explained
Image courtesy: BorgWarner
Image courtesy: Siemens
Tire(s)
Image courtesy: Volvo Cars

## Slide 5: System overview
Inverter
Battery
system
Gearbox
Differential
Wheel
Wheel
Electric
Machine
Real Power Voltage Current
Complex Power
3xVoltage 3xCurrent
Frequency Amplitude Phase delay
Mechanical
Power, Speed, Torque, Force
𝑉𝐷𝐶 (V)
𝐼𝐷𝐶 (A)
𝑃𝐷𝐶 (W)
𝑉𝐴𝐶 (V)
𝐼𝐴𝐶 (A)
𝑆𝐴𝐶 (VA)
3x
3x
Ω𝐸𝑀 (rad/s)
τ𝐸𝑀 (Nm)
𝑃𝐸𝑀 (W)
3x
Ω𝐺𝐵 (rad/s)
τ𝐺𝐵 (Nm)
𝑃𝐺𝐵 (W)
𝐹𝐿 (N)
𝑣𝐿 (m/s)
𝐹𝑅 (N)
𝑣𝑅 (m/s)
Ω (rad/s)
𝐿
𝜏𝐿 (Nm)
𝑃𝐿 (W)
Ω𝑅 (rad/s)
𝜏𝑅 (Nm)
𝑃𝑅 (W)
Road
Road
Electrical
Electric drive: DC in, torque out

## Slide 6: Electric Machines – Types, parts and names

## Slide 7: Three-phase machines
Image source: GE Power
Electric machines usage in industry from 1890s.
Grid generators, pumps, fans, toys, appliances…
For cars? First from 1990 with GM EV1, Toyota RAV4 EV and more.
Few watts
Many megawatts

## Slide 8: EM high-level energy conversion
Electric machine energy conversion chain:
Voltage  Current  Magnetic flux  Torque  Speed
Electric Machine
Ψ = Magnetic flux
τ = Torque
ω = Speed
ua,b,c = voltage
Inverter
coils
ia,b,c = current
Drive axle
coils
coils

## Slide 9: Electric Machine Types
Rotating machine
PM
excitation
Rotor Excitation, e.g.
Permanent Magnet
AC Synchronous
Reluctance
Surface PM
AC Asynchronous
Uni-polar
Wound rotor
Alu/Cu squirrel
cage rotor
Universal machine
Low power applications.
Vacuum cleaner, washing machine,
kitchen appliances
Legacy traction applications, toys
Large grid generators
Doubly salient
Switched
reluctance
Synch. reluctance
Inset PM
Interior PM
PM/rel hybrid
Most common for automotive traction
Most common for hybrids
BLDC
Most common industrial motor
Good for automotive traction
Commutated machines
DC AC
Electric
excitation

## Slide 10: Automotive electric machine examples
”A Look Inside The Tesla Model 3,
Chevy Bolt, and BMW i3”
(7:25-11:37)
https://youtu.be/pgu6mkKZwNg?t=445
“Chevrolet Bolt EV Traction
Motor - Deep Dive”
(0-0:54 and 49:04 rotor 51:24 stator stack) https://youtu.be/APhRPSdmdmk
GM Chevrolet Bolt
BMW i3
Tesla Model 3

## Slide 11: Parts and names (1/5)
End plate
Cooling Fan
Drive End
(DE)
Non-Drive
End (NDE)
Connection
box
Housing
Stator windings
Rotor
Typical industrial motor (induction machine)

## Slide 12: Parts and names (2/5)
Stator windings
End winding / Winding overhang
Stator
core
Typical industrial motor (induction machine)
Active length
“Magnet wire” =
Enamelled copper

## Slide 13: Parts and names (3/5)
“Electrical steel” =
Laminated Silicon Steel
Stator core
Stator slot
Stator tooth
Core laminates
Tesla Model 3 rear EM stator laminate by Stefan Skoog
Stator back/
stator yoke

## Slide 14: Parts and names (4/5)
Squirrel cage
(Cu or Al)
Typical industrial motor (induction machine)
Rotor core
Rotor laminates
(electrical steel)
Rotor axle
Roller Bearing
Roller Bearing

## Slide 15: Parts and names (5/5)
Stator
Rotor
Photos of Tesla Model 3 rear EM laminates by Stefan Skoog
Torque is produced in “inside the airgap”.
Air gap length =
Stator Inner radius – Rotor Outer radius (Usually ca 1.0 mm)
Active volume =
Active length * Stator outer radius² * Pi

## Slide 16: 3-phase sinusoidal current feed
When each stator coil is fed with an individual sinusoidal,
each 120 degrees separated, the total magnetic flux will appear to rotate.
The rotor in this illustration is fed with DC, i.e. equivalent to a permanent magnet.

## Slide 17: Electric Machines – Electrical properties

## Slide 18: The magnetic-electric circuit (revisit)
For low currents and rotor standstill, each phase winding behave electrically like a big inductance.
Each phase winding are usually simplified by just one inductance in electrical diagrams.
All phase windings are usually Y-connected to form a three- wire system without neutral conductor.
N
S
A+
A-
B+
C+
C-
B-
Equivalent electrical circuit
A+
A-
B+
B-
C+
C-
A
B
C

## Slide 19: Some basic behaviors of EMs
Machine constant, depends on machine design, e.g.
geometry, winding layout
A coil exposed for a varying magnetic field (e.g. rotating rotor) will induce a voltage in the coil – Back-ElectroMotive Force (BEMF)
Machine rotational speed in rads/seconds
𝐸𝐵𝐸𝑀𝐹 = 𝐾𝑚 ω 𝛷
Magnetic flux from rotor, either from permanent magnets (Φ𝑃𝑀) or electromagnets (Φ𝐸 )

## Slide 20: Electric Machine Equivalent Circuit
The simplest useful electrical model of an electric machine:
Following equations describing the machine in steady-state (rotating at constant speed):
R L
i(t)
+
u(t)
-
𝑈 = 𝐼𝑅 + 𝐸
ω
𝑚
𝐸𝐼
𝑇 = = 𝐾 𝛷𝐼
𝑃𝑒𝑙𝑒𝑐𝑡𝑖𝑐 = 𝑈𝐼 𝑃𝑚𝑒𝑐ℎ𝑎𝑛𝑖𝑐𝑎𝑙 = 𝐸𝐼
𝑃𝑅𝑒𝑠𝑖𝑠𝑡𝑖𝑣𝑒 = 𝑅𝐼2
𝐸 = 𝐾𝑚ω 𝛷
+
-
+
e
-

## Slide 21: Three-phase Full Equivalent Circuit
Equivalent circuits
Looks nice (explicit and continuous)
Solves fast
Many of the “constants” vary with current, speed, temperature
Hard to extract/derive parameters
𝑃𝑅𝑒𝑠𝑖𝑠𝑡𝑎𝑛𝑐𝑒 = 𝑅𝑠(𝑖2 +𝑖2 +𝑖2)
𝑎 𝑏 𝑐
Single phase representation Three phase representation
𝑢𝑎
𝑢
𝑏
𝑢𝑐
=
𝑅 0 0
0 𝑅 0
0 0 𝑅
𝑖𝑎
𝑖
𝑏
𝑖𝑐
+
𝐿 𝑀 𝑀
𝑀 𝐿 𝑀
𝑀 𝑀 𝐿
𝑑
𝑑𝑡
𝑖𝑎
𝑖
𝑏
𝑖𝑐
+
𝑒𝑎
𝑒
𝑏
𝑒𝑐
𝑃𝑒𝑙𝑒𝑐𝑡𝑟𝑖𝑐𝑎𝑙 = 𝑢𝑎𝑖𝑎 + 𝑢𝑏𝑖𝑏 + 𝑢𝑐𝑖𝑐
𝑃𝑚𝑒𝑐ℎ𝑎𝑛𝑖𝑐𝑎𝑙 = 𝑒𝑎𝑖𝑎 + 𝑒𝑏𝑖𝑏 + 𝑒𝑐𝑖𝑐
𝑒𝑎𝑖𝑎 + 𝑒𝑏𝑖𝑏 + 𝑒𝑐 𝑖𝑐
𝑇 =
𝜔𝑟
PMSM and IPM equivalent circuit model

## Slide 22: A simpler way of representing EM behavior
Look-up-tables
Easy to extract from FEA*
Can include many non- linear effects
Solves reasonably fast
Lots of data tables to handle
Need lots of memory
Needs comprehensive FEA to extract data
Graph: Nissan Leaf EM of total losses, data map: 39x60 operating points
*FEA = Finite Element Analysis

## Slide 23: Electric Machines – Typical Performance

## Slide 24: ICE vs EM typical performance (1/2)
ICE has to rotate to be able to produce torque
EM can produce maximum torque from standstill
Image courtesy: Branko Ban for University West
Typical Internal Combustion
Engine performance
Typical Electric Machine
performance

## Slide 25: ICE vs EM typical performance (2/2)
Maximum ICE ca 36% (best-in-class 41%) Maximum EM efficiency ca 90% (best-in-class 97%) EM can charge traction battery in generator mode ICE maximum efficiency is rarely utilized
Typical Internal Combustion
Engine performance
Typical Electric Machine
performance

## Slide 26: Electric and hybrid vehicle powertrains
T (Nm)
+Tmax
-Tmax
Maximum torque
 More current
(inverter and EM cooling)
Maximum power
 Battery performance and Inverter size
Maximum speed
 Inverter speed and EM rotor design
N (rpm)
EM shaft speed
EM Shaft torque
Typical performance envelope, and what components that limit performance.
EMs with inverters can be used in reverse rotational direction with same performance.

## Slide 27: Performance examples
For automotive electrical machines

## Slide 28: Performance examples
Car manufacturers rarely publish full performance on their electric machines.
Measurements are complicated and require big, expensive equipment to perform.
Some 3rd party companies are offering measurement data, usually for a high price.
One entity is offering lots of data for free: US Department of Energy, Oak Ridge National Laboratory
Nissan Leaf (generation 1)

## Slide 29: Nissan Leaf 2012
Map of eMachine + inverter combined. Gearbox losses missing!
280 Nm, 80 kW traction
machine. 56 kg.
* Benchmarking State-of-the-Art Technologies. Tim Burress.
2013 U.S. DOE Hydrogen and Fuel Cells Program and Vehicle Technologies Program Annual Merit Review and Peer Evaluation Meeting
Measured at 375 V DC

## Slide 30: Efficiency
Typical efficiency numbers for EM: 90-97 % peak
  As a reference: Premium Efficiency (IE3) industrial machines reach peak efficiency of 95.4% efficient at 110 kW rating
Typical efficiency number for EDU: 88-95 % peak
  About half of the losses are in EM, rest is split fairly even between inverter and gearbox.
Specific power
A metric used to judge how compact the electric machine or EDU is in total, regardless of power and size: Power-to-weight-ratio.
Example Prius 2017 MG2: 53 kW / 18.2 kg = 2.9 kW/kg (max power / active parts weight)
Industrial standard machines: Automotive electrical machines: Experimental aircraft electric machines:
0.1 kW/kg
1.0-3.5 kW/kg
10-20 kW/kg

## Slide 31: Design and modeling of EMs
FEA and Simulink Models

## Slide 32: Finite Element Analysis (FEA)
What is FEA, and why and when is it needed?
Problem Background
Magnetic circuits are highly non-linear when used at the edge of their performance limits
  Why are they used at the edge of performance limits?
  To reach high performance (power, torque) in a small volume or low weight
Analytical models offer very limited accuracy for EMs
The FEA solution
Model the motor in CAD, and then break it down in thousands of mathematically “ideal” pieces (meshing) and solve the non-linear electromagnetic equations for each piece.

## Slide 33: FEA tools
List of popular FEA tools for rotating Electric Machines used in automotive industry:
Ansys Electronics / Ansys Maxwell
MotorCAD (Ansys/Motor Design Ltd)
JMAG
Comsol
FEMM
Altair Flux
Dassault Opera

## Slide 34
FEA examples (1/2)
Video: Draw of Q12p10 tooth-coil machine in Ansys Electronics https://youtu.be/TC0tZm9Cox4

## Slide 35: FEA examples (2/2)
Draw 2D representation of the magnetic circuit, and define electrical input/outputs
Find the smallest unique magnetic
section of the machine
Define a symmetric and
robust mesh for FEA.
Make sure the mesh is detailed and symmetric in the airgap
Three layers of symmetric triangles in the airgap is a good start
Source: “Component and system design of a mild hybrid 48 V powertrain for a light vehicle”, PhD defence presentation by Stefan Skoog, 2020

## Slide 36: MotorCAD data export
Nissan Leaf motor demo by Felix Mannerhagen (EDS600 via HV play)
Assumptions:
  Temperature of EM parts steady-state
  MTPA – Maximum Torque Per Ampere solved by MotorCAD
  Robust closed-loop current feedback control implemented
𝜔
𝑇
𝑃𝑙𝑜𝑠𝑠
𝑃𝑒𝑙
𝐼𝑝ℎ𝑎𝑠𝑒
𝑈𝑝ℎ𝑎𝑠𝑒
𝑃𝐹
EM

## Slide 37: Assignment 3
EM performance and Simulink Model3

## Slide 38: New features in “Model3”
EM block
  Running from look-up-tables from MotorCAD
New init file (‘init_Model3.m’)
  Executed automatically every time you press ‘simulate’ in Simulink
  This is the only init file you need to worry about (all other init-files removed)
  Plenty of comments inside to explain how it works
  All configurations & parameters are found in this file!
  Automatically imports data from MotorCAD data file(mat-file)
  Optional drive cycle (mat-file)
For instruction for Assignment 3, see Canvas page!

## Slide 39: Bonus slides
Optional deep-dive

## Slide 40: EM manufacturing
Renault Electric Motor Assembly https://youtu.be/WSH983zUNIo
Audi Factory - E-Engine Production https://youtu.be/7T6iCknDCEg

## Slide 41: Overview of automotive EMs
Tesla Model 3 and Y Modular Motors
Weber Auto (28 min)
Model Y E16: Electric Motor Comparison MY-M3, Industry review of Electric Motors Munro Live
(17 min)